Architectural Components Group, Inc.

521 George St.

Marshfield, MO 65706

417-869-6777  /  417-869-7888 fax

info@acgiwood.com / acgiwood.com

ARCHITECTURAL SPECIFICATIONS FOR

CONCERTO™ SERIES 1

FLAT PANEL WALL SYSTEM

[Project Name]

[Project Location]

PART 1 — GENERAL

1.1 Description of Work:

- Work Included: Provide Architectural Components Group, Inc. Concerto™ Flat Panel Wall System, CW1-xxxx-C where shown on architectural drawings, and as specified in this specification.

1.2 Quality Assurance:

- Architectural Components Concerto™ Wall System for this project shall maintain the quality as instituted by the architect or A.W.I.

- Manufacturing Standards: Panels shall be constructed according to strict adherence to manufacturer’s specifications. Dimensions shall be maintained within 1/16”.

- Design Criteria: Manufacture of Concerto™ Wall System, CW1-xxxx-C shall be installed true and plumb to within a tolerance of 1/8” within 8’ of length.

- Product Construction: Wood shall be kiln dried to 10%. Cracking, checking and warpage of members will not be acceptable.

1.3 Submittals:

- Technical Data: Submit manufacturer’s data and installation instructions.

- Shop Drawings: Submit 4 copies of shop drawings showing all areas involved, attachment conditions and perimeter circumstances.

- Submittal Sample: Submit 1 product sample for approval by architect.

1.4 Delivery, Storage and Handling

- Material MUST be STORED and installed only in secured ambient environment (humidity min. 25% - max. 55%, temperature not to exceed 86 degrees).

- Windows, doors and all wet-work must be completed before unpacking and installation. Handle carefully to avoid damage.

- Contractor shall be responsible to store all panels, moldings and doors in a flat condition protected from jobsite conditions.

PART 2 — PRODUCTS

2.1 Acceptable Manufacturer:

Architectural Components Group, Inc.  521 George St. Marshfield, MO 65706

Phone (417) 869-6777	Fax (417) 869-7888

2.2 Product Type

- Product Configuration: Concerto™ Wall System shall be product: CW1-xxxx-C

Nomenclature for CW1-4896-C:

CW1 = Concerto™ Wall Series 1

4896 = a panel 48” wide x 96” tall

C = 3/4” thick substrate

- Specie: System shall consist of specie wood veneer [e.g., cherry, quartered, slip-matched].

- Perforations: Panels shall or shall not have perforations. If perforations, then Xmm holes Xmm O.C. with perforation pattern parallel, offset, or xx/xx pattern. Some available perforation patterns are: 6mm or 8mm holes, 16mm or 32mm O.C.

- Fire Rating: Wood panels shall achieve a Class I(A) or Class III(C) fire rating.

- Finish: Wood veneer finish shall utilize ACGI clear finish with satin sheen or specify custom stain to match architect sample.

- Certification: Wood veneer shall or shall not be FSC certified. The substrate material shall or shall not be FSC certified. If FSC, then Chain of Custody shall or shall not be required.

- Substrate material shall or shall not be manufactured with no added urea formaldehyde.

- Accompanying Trim: Shall be product: CWT-xxx (as per architect's drawings).

- Attachment System: Concerto™ Wall System shall be mounted using ACGI Concerto™ extrusions and mounted according to manufacturer’s suggested method of mounting as outlined in the accompanying instruction guide.

PART 3 — EXECUTION

3.1 Installation

- The Concerto™ wood wall system shall be handled and installed with care in order to prevent surface and structure damage. Field cutting shall be kept to a minimum and performed as recommended by manufacturer.

- Contractor shall clean all panels prior to installation according to manufacturer’s recommended maintenance procedures. Upon completion of installation, panels shall be inspected and cleaned as needed.

PART 4 — WARRANTY

4.1 Product Warranty

- Architectural Components Group, Inc. shall warranty the Concerto™ wood wall system against manufacturer’s defects up to one year. Changes in finish or dimensions due to ultra violet light, excessive temperature or humidity conditions and/or abuse of any kind shall void any warranties from ACGI.

- Install conditions for the area should remain for the proper occupied conditions of humidity and temperature (humidity min. 25% - max. 55%, temperature not to exceed 86 degrees).

- The contractor shall warranty for one year all work from final acceptance of completed work.